## Slide 1
Ke Xu, Ph.D.
Mobile Video System

## Slide 2
Overview
Architecture
2
Decoder
3
Encoder
5
4
1
MISC

## Slide 3: A Competitive Solution
Fundamentals
Codec & Features
Power
Streaming & Video Chat
Performance
Editing & Sharing
Video Quality
Die Size
4K 30/60/120fps
4K thermal issues
HEVC, SHVC, VP9, 10 bit
Lowest possible cost
Pre & post-processing
Enabling fast editing & Sharing
Video communication over Modem
Video HW for other use-cases
Video analysis, Computer vision
Opportunities to differentiate

## Slide 4: Market Trends

## Slide 5: Basic Usecase
WiFi Display
Camcorder
Video Playback
Video Streaming
Video Telephony
Encoder + decoder
Miracast 2.0
4K, 10bit, 422 or 444
Encoder
1080p or UHD
Not 4K yet
Decoder
4K 60, 4K 120?
Decoder
Encoder + decoder

## Slide 6: Video Codec Solution
  Hardware IP Core Dedicated Video IP core.
  DSP Video Fully or partially (hybrid) DSP accelerated based solutions.
  Software Codecs Optimized software solutions (licensed or developed in-house).

## Slide 7
Overview
Architecture
2
Decoder
3
Encoder
5
4
1
MISC

## Slide 8: System Overview
A: host and ARM communication via general registers
B: host and ARM data exchange via system memory
C: host access HW SWI registers directly (debug mode)
D: ARM controls HW via SWI (normal mode)
E: FW access data in system memory
F: HW access data in system memory

## Slide 9: Software Overview
Windows on ARM
…
QNX
Windows Phone
Android
…
Firmware
Video Driver
Multimedia Framework
Application
Hardware
User space - Java
User space – C++
Kernel space

## Slide 10: Firmware Tasks
HW side
  Frame level interaction between FW/HW
  Slice interaction for H264/H265
SW side
  SW queue in bitstream and YUV buffers.
  FW/HW finish encoding/decoding and return to buffers
Multiple session support
Data processing for encoder
  Frame level rate control
  Frame type decision
  Reference frame management
    Different GOP structure
    Long term reference
  Header encoding
Data processing for decoder
  Start code search
  Frame accumulation
  Frame/slice header parsing
  Reference frame management

## Slide 11: Hardware Architecture

## Slide 12: Architecture Options
1. Shared
2. High
Performance
3. Multi-core

## Slide 13: Concurrency Measurement (max frame rate)
Some MTK chipsets don’t have significant frame drop for simultaneous encode & decode

## Slide 14: Engine Configuration

## Slide 15
Overview
Architecture
2
Decoder
3
Encoder
5
4
1
MISC

## Slide 16: Decoder Dataflow

## Slide 17
Codec | Standard |  |  | Core Requirement | 
 | Profile | Level | Max Performance | Max. Sessions | Processing Capacity
HEVC | Main/Main Still Picture/Main10 | 5.1 | 4096x2160, 60fps, 160Mbps | 1 | Max resolution & fps: 4096x2160, 60fps Max bit-rate: 240 Mbps Main Still Picture Profile supports resolution up to 8192x4320 with TBD fps.
 |  | 4.1 | 2048x1080,60fps, 50Mbps | 4 | 
 |  | 4.0 | 1080p, 32fps, 30Mbps | 8 | 
 |  | 3.1 | 720p, 33.7fps, 10Mbps | 16 | 
H264 | Baseline, Main, High, High-10, High-10 Intra | 5.1 | 4096x2304, 26.67 fps, 240Mbps | 1 | Max resolution & fps: 4096x2160, 60fps Max bit-rate: 300 Mbps
 |  | 4.2 | 2048x1080, 60fps, 50Mbps | 4 | 
 |  | 4.1 | 1080p, 30fps, 50Mbps | 6 | 
 |  | 4.0 | 1080p, 30fps, 20Mbps | 8 | 
 |  | 3.1 | 720p, 30fps, 14Mbps | 16 | 
 | High 4:2:2, High 4:2:2 Intra | N/A | 4096x2160, 45fps, 180Mbps |  | Max resolution & fps: 4096x2160, 45fps Max bit-rate: 180 Mbps
 | High 4:4:4 Predictive, High 4:4:4 Intra CAVLC 4:4:4 | 5.1 | 4096x2304, 26.67 fps, 240Mbps | 1 | Max resolution & fps: 4096x2160, 30fps Max bit-rate: 240 Mbps Note: High 4:4:4 profiles support up to 10 bits
VP9 | - | - | 4096x2160, 60fps | 1 | Max resolution & fps: 4096x2160, 60fps Max bit-rate: 320 Mbps
VP8 | - | - | 4096x2160, 60fps | 1 | 
MPEG4 | SP | 8 | 1080p, 30fps, 20Mbps | 8 | Max resolution & fps: 1080p, 240fps Max bit-rate: 320 Mbps
 | ASP | 5 | 720x576, 30fps, 8Mbps | 16 | 
DivX 3/4/5/6 | HD |  | 1080p, 30fps, 20Mbps | 16 | 
 | Home Theater |  | 720p, 30fps, 20Mbps | 16 | 
H263 | P0 | 70 | 720x576, 30fps, 16Mbps | 16 | 
Sorenson | V0/V1 |  | 720x576, 30fps, 16Mbps | 16 | 
MPEG2/1 | Main | High | 1080p, 30fps, 80Mbps | 4 | Max resolution & fps: 1080p, 240fps Max bit-rate: 320 Mbps
VC1 | SP | Medium | 352x288, 15fps, 384Kbps | 16 | Max resolution & fps: 1080p, 240fps Max bit-rate: 360 Mbps

## Slide 18
Codec | Host | Video Controller ARM9 | Video HW
HEVC | Stream queuing Buffer management | SPS, PPS, SEI Slice header/APS Reference frame management Buffer management for 2-stage SP | Slice data Header parsing assistance
H264 | Stream queuing Buffer management | SPS, PPS, SEI Slice header Reference frame management Buffer management for 2-stage VSP | Slice data Header parsing assistance
VC-1 | Stream queuing Buffer management Metadata processing | Sequence layer Entry-point layer (AP) Metadata (SP/MP) Picture header except bit plane | Bit plane parsing Slice header Slice data
MPEG2 | Stream queuing Buffer management | Sequence and extension headers Picture/GOP, extension headers & user data | Slice header Slice data
MPEG4/ DivX4,5,6 | Stream queuing Buffer management | Visual object sequence header Visual Object header Visual Object Layer header | MB data RM/HEC
DivX3.11 H263/ Sorenson | Stream queuing Buffer management Metadata | Picture header | Picture data
VP8/9 | Stream queuing Buffer management | Frame header Probability update Buffer management for 2-stage VSP | Frame data

## Slide 19: SDE Performance
Tier | Spec | Cycle count/16x16 | Upper bound Bitrate performance | Required Bin Processing Rate
HT/MT (Turbo) | 4K60@ 533Mhz | 215 | 1080p@30 8 channels 400 MBps | 1.2 Bins/cycle
HT/MT (Nominal) | 4K30@ 333Mhz | 306 | 1080p@30 4 channels 200 MBps | 0.85 Bins/cycle
ULT-H (Turbo) | 1080p90@ 326 MHz | 400 | 1080p@90 1 channel 150 Mbps | 0.6 Bins/cycle
ULT-H (Nominal) | 1080p60@ 217 MHz | 400 | 1080p@60 1 channel 100 MBps | 0.6 Bins/cycle

## Slide 20
Overview
Architecture
2
Decoder
3
Encoder
5
4
1
MISC

## Slide 21: Encoder Data Flow

## Slide 22
Codec | Host | Video Controller ARM9 | Video HW
HEVC | Frame queuing Buffer management | Frame and slice level RC SPS and PPS packing Slice header packing Reference frame management Buffer management for 2-stage VSG | All MB encoding MB level RC Stream generation
H264 | Frame queuing Buffer management | Frame and slice level RC SPS and PPS packing Slice header packing Reference frame management Buffer management for 2-stage VSG | All MB encoding MB level RC Stream generation
MPEG4 | Frame queuing Buffer management | Frame and packet level RC Visual Object Sequence packing Visual Object header packing Visual Object Layer header packing Data partition management | All MB encoding MB level RC Stream generation
H263p0 | Frame queuing Buffer management | Frame and GOB level RC Picture header packing Plus header packing | All MB encoding MB level RC Stream generation
On2 VP8/9 | Frame queuing Buffer management | Frame level RC Frame header packing Probability update | All MB encoding MB level RC Stream generation

## Slide 23: Engine Tasks (1)
Component | Task
HW SDE | Arithmetic Encoding for slice data QP prediction
HW SE | Top/Left Neighbor fetching, Scaling list/Lambda fetching, Collocated MV fetch and data store MV reconstruction/Intra mode Prediction/BS computation Residue data Inverse Scan Command preparation and dispatching for TE/PE/FE Feedback to TE on RCI Pipeline control for MEC Binstream/Bitstream packing

## Slide 24: Engine Tasks (2)
Component | Task
HW MEC | Subsampled Search Engine Integer Search Engine Fractional Search Engine MVP (Merge Candidate derivation, Pruning, Skip/Direct candidate calculation) MVP (Buffer maintenance for neighboring MVs) Pack the final Modes/MVs to SE
HW TE | Forward Quant/Transform Inverse Quant/Transform Rate control Slice boundary detection Zero Block Detection Redo Intra Prediction
HW PE | Reference Pixel Fetch Spatial/Temporal Prediction Redo Intra Prediction Pixel reconstruction
HW FE | In-loop filtering SAO Algorithm + SAO Processing

## Slide 25: Encoder Evolution
 | 1st Gen | 2nd Gen | 3rd Gen
Codec | H.264, MPEG4, H.263, VP8 | H.264, MPEG4, H.263, VP8, HEVC | H.264, MPEG4, H.263, VP8, HEVC, VP9
Encoding Quality | 1080p30 | 4K30 | 4K30, 4K60
Search Range | ±96 x ±48 (1ref) ±64 x ±32 (2ref) | ±160 x ±80 (1ref) ± 96 x ±48 (2ref) | ±160 x ±80 (1ref) ± 96 x ±48 (2ref)
Cost Metric | SAD, SATD | SAD, SATD, SAITD | SAD, SATD, SAITD
Block Size | 8x8 (min), 16x16 (max) | 8x4/4x8 (min), 32x32(max) | 8x4/4x8 (min), 64x64(max)
Slicing | Byte-based, MB-based | Byte-based, LCU/MB-based, accurate byte-based | Byte-based, LCU/MB-based, accurate byte-based
WFD Quality | No specific tools | Transform-skip, re-do intra | Transform-skip, re-do intra, 4:4:4

## Slide 26
Rate Control

## Slide 27: Background
Basics
  Changing Quantization Parameter (QP)
  Skip (not encode) some frames
Modes
  Variable Bit-Rate(VBR)
    Maintain constant quality as much as possible
    Allow bitrate to fluctuate within bounds
  Constant Bit-Rate(CBR)
    Reduce convergence time to target bit-rate as much as possible
    Maintain constant bit-rate within fixed time intervals (e.g. 1s)

## Slide 28: Applications
  Best quality
  Storage mode
  Post processing (editing)
  Camcorder
  WFD
  MMS
  Aggressive VT
  eMBMS
  HTTP streaming
  Video telephony
  Cisco telepresence
  ALS
  WFD
CBR
CBR+
VBR+
VBR

## Slide 29: Rate Control

## Slide 30: Perceptual Quantization
Better perceptual quality at same bitrates
  Make use of Human Visual System (HVS) model
  Less sensitive to high frequency components

## Slide 31
MEC

## Slide 32: Motion Estimation Control

## Slide 33
Overview
Architecture
2
Decoder
3
Encoder
5
4
1
MISC

## Slide 34: MISC
Performance
Power
Scalability
Error Concealment
Value Added Features
Research

## Slide 35
Performance

## Slide 36: Performance
Static performance and BW analysis
  Linear vs. tile format
  Frame compression ON vs. OFF
  Separate vs. unified RPB/DPB
System-level static analysis
  With system architecture team
Dynamic performance and BW analysis
  Latency curves

## Slide 37: Video Level Static Analysis
Video heavy use cases
  Worst case: decode 4K@60fps 10bpp + WFD 1080p@60fps 4:4:4
Source of BW variations
  Various content for decoder
  Start code search for decoder
  Reference read BW variations for encoder

## Slide 38: System Level Static Analysis
Video
Decode
MDP
Rotate
Buffer
MDP
Graphics Buffer
Buffer
MDP
Rotate
MDP
Write back
Video
Encode
Buffer
Buffer
Display Picture Buffer
4096x2160p60 4:2:0 8bpc
Compressed
Main Panel
4096x2160p60 4:2:0 8bpc
MPR @ 60FPS ARGB32
4096x2160p60 4:2:0 8bpc
1080p60 4:2:0 8bpc
Compressed

## Slide 39: Dynamic Latency Tolerance
Chart: DDR Latency(clks)
| 1 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400
Tiled 8-2-2 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14
Size-8-2-2 | 15.6 | 15.9 | 16.2 | 16.6 | 17.1 | 18.4 | 20 | 21.6 | 23.2
Size-20-15-15 | 14.9 | 15.2 | 15.5 | 15.8 | 16.1 | 17.2 | 18.6 | 20 | 21.5
Size-40-30-30 | 14 | 14 | 14 | 14.1 | 14.4 | 15.3 | 16.7 | 18.1 | 19.5
Size-60-45-45 | 14 | 14 | 14 | 14 | 14 | 14.2 | 15.3 | 16.7 | 18.1
Size-Infinte | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14.1 | 14.3
TargetTime | 15.8333 | 15.8333 | 15.8333 | 15.8333 | 15.8333 | 15.8333 | 15.8333 | 15.8333 | 15.8333
Size-80-60-60 | 14 | 14 | 14 | 14 | 14 | 14 | 14.3 | 15.3 | 16.6

## Slide 40: Performance Variations
Chart: Codec Performance across tiers (w/o DDR latency)
| Decode H264 | Decode HEVC | Encode LQ | Encode HQ
LT | 400 | 920 | 1050 | 2100
MT | 322 | 363 | 425 | 510
HT | 212 | 212 | 328 | 406

## Slide 41: QoS

## Slide 42
Power

## Slide 43: CPU Encode
  4K@30 encoding with A53 alone
  4xA53, 95%@941MHz
  Average battery power 9.3W

## Slide 44: CPU Encode

## Slide 45: Frame Complexity
Chart: Decode time in ms @ 465 MHz
Vhigh
Vmid
Vlow
Example where per frame
complexity varies significantly

## Slide 46: DCVS

## Slide 47: HW Competitive Analysis
Chart: 1080p@30fps power comparison (mA)
| iPhone5s | Note3 (Exynos 5420) | Qualcomm
QTC_88 (AP) | 93 | 172 | 105
4k@30fps video playback capability
  iPhone5s does not truly support 4k30
  Exynos 5420 does not support 4K
Profile | Complexity | iPhone5s | Qualcomm
Baseline | Low | ü | ü
 | Medium | X | ü
 | High | X | ü
Main | Low/Medium/High | X | ü
High | Low/Medium/High | X | ü
Decoding
complexity
Chart: 1080p@60fps power comparison (mA)
| iPhone5s | Note3 (Exynos 5420) | Qualcomm
QTC_88 (AP) | 133 | 252 | 157

## Slide 48: Power Reduction
Chart: 4K 30 decode power - WQXGA Panel Power in mA @ Battery (3.7V)
| 8994 | 8994 With DCVS | 8996 With UBWC | 8996 with UBWC+DCVS
4K decode power - WQXGA Panel | 290 | 266 | 204 | 181
51mA due to design, process change
35mA due to BW compression
86 mA

## Slide 49: 4K Downscaling
Chart: 
| Original | Downscale & BWC | Apple A7
MDP | 1441 | 185 | 1700
Video | 736 | 779
CPU | 106 | 95
Others | 72 | 65
Bandwidth saving from 4K downscaler
MB/s
2355
1124
1700
Motivation: downscaler saves both BW and power
  52% reduction in bandwidth if the 4K output is (inline) downscaled to 1080p
  With this optimization, Q beats A by 51%
  Reduction in bandwidth directly contributes to an overall power saving of ~26% for the 4K decode

## Slide 50: 4K DCVS + Downscaling

## Slide 51
Scalability

## Slide 52: Scalability
Separate vs. merged encoder & decoder
  High tier: separate for performance and power collapse
  Mid/low tier: merged for area
Memory scalability
  L1, L2, L3 cache size
  On-chip memory size
Datapath scalability
  Multiple transform engine
  Pixel-level parallelism
Multi-pipe scalability
  4K 60fps and beyond
  VSP: multiple engines for consecutive slices/frames, HEVC WPP
  VPP: multiple engines for LCU rows (staggered by 2 MBs)
Bitrate scalability
  Multiple CABAC engines for bitrate > 400Mbps
Hybrid solution
  VSP in SW, VPP in HW
  MEC in HW, rest in SW, etc.

## Slide 53
Error Concealment

## Slide 54: Error Concealment
Error can be detected in following modules
  FW
  CCE
  SDE
  SE
Error detection in FW involves
  Range checking of SPS/PPS and slice header data
  Checking for lost NAL units
  Watch-dog timer in case of HW hangs

## Slide 55: Scenarios

## Slide 56: Error Concealment
Merge Mode concealment vs. Colocated concealment

## Slide 57
Value Added Features

## Slide 58: Value Added Features
Video stats for scene analysis
  [HW] Motion estimation, block texture, frame disparity, etc.
  [SW] Post processing
  [App] Scene change detection, object tracking, video analysis
Electronic Image Stabilization (EIS)
  Correct camera shake
  Compensate rolling shutter effect
Video over modem

## Slide 59
Research

## Slide 60: Research - H.266/NGVC

## Slide 61: Research - Screen Content Coding
HEVC extension (started April 2014)
  Synthetic (graphics & text)
  Intra block copying, palette mode, etc.
  Average improvement ~ 50%

## Slide 62: Thank you!

## Slide 63: Backup slides

## Slide 64: Team Organization
Video
VP
Algorithm & System Team
Director, >30
HW Team
Director, ~30
DV Team
Director, ~40
SW/FW Team
Director, ~50
Usecase analysis
Algo development
System architecture
Test vector generation
System modeling
Performance modeling
Power modeling
Microarchitecture
RTL
HW emulation
UVM framework
Functional verification
Coverage
Virtual platform
HW emulation
Software for playback, telephony, streaming, etc.
Various drivers
Usecase analysis

## Slide 66: Playback Power Analysis
Chart: Decoder 1080p30 - Power (mA at the battery 3.7V)
| A7 - iPhone 5s | 8974 Pro-XPM | 8974-Pro-55 | Exynos-5422 - S5 | Tegra4-Xiaomi MI3 | 8974 -Lumia 2520 | Intel-BayTrail
Decoder 1080p30 - Power (mA at the battery 3.7V) | 93 | 125 | 135 | 190 | 227 | 244 | 446
Chart: Decoder 4K30 - Power (mA at the battery 3.7V)
| A7 | 8974 Pro -XPM | 8974-Pro-55 | Exynos-5422 - S5 | Tegra4-Xiaomi MI3 | 8974-Windows Liquid | Intel-BayTrail
Decoder 4K30 - Power (mA at the battery 3.7V) | 190 | 310 | 345 | 322 | 543 | 390 | 619
Only plays simple Baseline clips
Not a commercial 4K solution

## Slide 67: Video Die Size
Re-evaluate practical worst case
Resource sharing (SRAM size reduction)
Low tier trade area for compression efficiency/video quality
Targeting PD optimization to improve utilization

## Slide 68: Die Size Reduction Roadmap

## Slide 69: Fastest HEVC Enablement

## Slide 70: My Roadmap
Step1
Video Codec
Step2
Differentiation
Step3
Computer Vision
Multi-standards
4K, 10bit
Area
Power
Performance
SW + FW + HW
Preprocessing
Postprocessing
IP/connected camera
  Video Stabilization
  120/240 fps encoding, 1/8th playback
Video surveillance
Video telephony
  Basic rate adaptation
  Dynamic FPS/resolution
  vs. Facetime/Skype
IoT/IoE
  Ultra low-cost solution
ADAS (automotive)
Augmented reality
Face detection
Face recognition
Hand gesture detection

## Slide 71: My Advantage
Vision
English
Strategic planning
15 years chip design
Connections
11 years video experience
10 years oversea
Communication
Leadership
Academy + industry